## Slide 1: Air-Conditioning - Terminology

## Slide 2: Important Terms
Refrigeration Cycle
Evaporation
Compression
Condensation
Refrigerant
Cooling Capacity

## Slide 3: Refrigeration Cycle
A Closed cycle of evaporation, compression, and condensation.
Transfer of Heat energy between two environments.

## Slide 4: Evaporation
The process of liquid becoming vapor/gas and it takes place in evaporator coil of an air-conditioner.
This part of the system gets cold to the touch (about 7°C/ 45°F) during it’s operation.

## Slide 5: Compression
The process of reducing the volume of a gas/ vapor is called compression.
The compressor pumps gaseous refrigerant to a high pressure and temperature.

## Slide 6: Condensation
The process of gas turning into liquid state is called condensation
It allows refrigerant to transfer heat without mixing.

## Slide 7: Refrigerant
The working fluid in refrigeration cycle is called refrigerant.
Modern AC's hydro flouro carbons that are inflammable, non-corrosive.
Most widely used refrigerant in residential AC's nowadays are R32.

## Slide 8: Cooling Capacity - Units
BTU or British thermal unit is generally used to measure Cooling capacity.
It can also be measured in Tons and Watts
Ton | Kilo Watts | BTUs/hr
01 | 3.6 | 12,000

## Slide 9: Quiz
01 Ton is equal to?
a) 120 Btus/hr.
b) 1,200 Btus/hr.
c) 12,000 Btus/hr.
d) 120,000 Btus/hr.